## Slide 1: Machine Learning Methods for Robust Uncertainty Quantification and Controller Approximation
Emilio Tanowe Maddalena’s Ph.D. exam
23.03.2023
Notes: Motivarte the research, try to tie the topics together, short
Delete kernels, add interpretations of what Im doing, my contributions again, non-stardard interpretations, empahsize the importance and connections among bounds, make a bigger deal
Pictures to illustrate the theorems
Sold KPC too short, and mneintion the optimal bounds could be dualized and incorporated there
Hit them with the math
Mention LA opt, and show Raphael’s video to sell it more
Don’t hold back on the math

## Slide 2: Agenda
PART 1
PART 2
PART 3
PART 4
Safely learning with kernels
Building temperature control through Gaussian process and model predictive control
Learning MPC controllers with pQP neural networks
Conclusions
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 3: Part 1
Safely learning with kernels
Published works:
Scharnhorst, Maddalena, Jiang, Jones. “Robust uncertainty bounds in reproducing kernel Hilbert spaces: A convex optimization approach.” IEEE Transactions on Automatic Control (2022).
Maddalena, Scharnhorst, Jones. “Deterministic error bounds for kernel-based learning techniques under bounded noise.” Automatica (2021).
Maddalena, Scharnhorst, Jiang, Jones. “KPC: Learning- based model predictive control with deterministic guarantees.” L4DC (2021).
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 4: Introduction
The final goal: carry out regression with hard error-bounds.
Motivation: deterministic, robust analysis and control of dynamical systems.
What family of functions to consider?
What complexity measure to use?
How to estimate uncertainty?
Notes: Goal: introduce kernels and RKHSs

## Slide 5: Introduction
Kernels and their RKHSs
More rigorously, a consistent and valid inner-product has to be defined on the superset. Also, the closure of a set is always closed.
The inner-product is defined as
Pre-Hilbert space
The actual Hilbert space
We will focus on positive-definite and strictly positive-definite kernels only.

## Slide 6: Introduction
Kernels and their RKHSs
The RKHS of certain PD kernels is dense in the space of continuous functions.
Notes: Goal: introduce kernels and RKHSs

## Slide 7: Results
Hard error-bounds in a kernelized setting
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 8: Results
Hard error-bounds in a kernelized setting
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 9: Results
Model-free uncertainty bounds in a kernelized setting
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 10: Results
Model-free uncertainty bounds in a kernelized setting
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 11: Examples
A simple function approximation problem
Optimal vs closed-form bounds (KRR model) with different regularization constants

## Slide 12: Results
Model-free uncertainty bounds in a kernelized setting
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 13: Examples
A simple function approximation problem

## Slide 14: Examples
Control sequence validation
CSTR system
Constraints
Desired equilibrium
A KRR model was learned from data and a certainty equivalence-based OCP was designed to drive the system close to the desired equilibrium from 4 distinct initial conditions, yielding (open-loop) sequences of control actions…
How to verify if these will lead to constraints violations?
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 15: Examples
Control sequence validation
CSTR system
Constraints
Desired equilibrium
Collect data by solving the same OCP at multiple initial conditions: d = 800 with a noise bound = 0.06
Learn multi-step ahead models and estimate the underlying RKHS complexity: isotropic SE kernel, 5-fold cross validation, 120% of norm augmentation
For each control sequence to be validated, query the kernel bounds (closed-form or optimal) and verify if they violate the system constraints
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 16: Examples
Control sequence validation
Phase portraits of the CSTR system under the same control inputs, but different uncertainty quantification techniques.
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 17: Examples
State trajectories of the CSTR system under the same control inputs, but with different uncertainty quantification techniques.
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 18: Examples
Kernel predictive control
Inverted pendulum
Constraints
Desired equilibrium
Multi-step kernel models
Robustifying constraints
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 19: Examples
Naïve kernel-based MPC
KPC predictions
KPC
Sampling period of 0.2 s, prediction horizon N=8, 100 data-points for each regression task (8 in total), noise bounds of 0.01, isotropic SE kernel, MLE estimation, and a norm augmentation factor of 300% to estimate the underlying RKHS norms.
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 20: Conclusion
Final remarks and future investigations
Kernel-based regression error-bounds were extended to handle noisy data
Novel uncertainty quantification techniques were put forward based on convex optimization
Applications were presented in the area of analysis and design of control systems
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 21: Conclusion
Final remarks and future investigations
Kernel-based regression error-bounds were extended to handle noisy data
Novel uncertainty quantification techniques were put forward based on convex optimization
Applications were presented in the area of analysis and design of control systems
Directions for possible future investigations include:
  Establishing continuity properties for and
  Covering the case of uncertain inputs
  Devising a kernel-based MPC algorithm that is optimistic rather than pessimistic
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 22: Part 2
Building temperature control through Gaussian process and model predictive control
Published works:
Di Natale, Lian, Maddalena, Shi, Jones. “Lessons learned from data-driven building control experiments: Contrasting Gaussian process-based MPC, bilevel DeePC, and deep reinforcement learning.” CDC (2022).
Maddalena, Müller, Dos Santos, Salzmann, Jones. “Experimental data-driven model predictive control of a hospital HVAC system during regular use.” Energy and Buildings (2022).
Maddalena, Lian, Jones. “Data-driven methods for building control—A review and promising future directions.” Control Engineering Practice (2020).
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 23: System overview
Notes: We’ll now switch gears and explore the control problem a bit.
I will describe a building and its HVAC system located in Campo Grande, Mato Grosso do Sul, Brazil. BTW, HVAC stands for heating, ventilation and air-conditioning.
Okay. Here’s Campo Grande, a city located in the central-western part of the country.

## Slide 24: System overview
Notes: A couple of years ago we established this partnership with a public hospital named Hospital São Julião, where we agreed to deploy a number of sensor networks to monitor the local HVAC plant and propose new control strategies for it.
The hospital is a large complex with over 30 buildings, but we were concerned with only the surgery center, the one in the top photo.
More specifically, the ophthalmology section of the surgery center, located on its West end.
There are two operating rooms and one waiting room, so three thermal zones in total.
There are no radiators in there, and cooling is achieved by pumping clean cold air into the zones through these outlets installed on the ceiling. That’s what we call a forced-air system.
How is this air produced?

## Slide 25: System overview
Notes: WELL, right to the side of these three rooms, you have a separate space where the HVAC plant is.
It’s composed of air-handling units (aka AHUs). There are large fans inside of them, as well as particle and bacteria filters to purify the air, and coils to bring down the temperature. These equipment collect air from the external environment and treat it beofre pumping it into the rooms.
Through these coils runs cold water supplied by a central chiller. The flow of water can be regulated by opening and closing the valves you see in this picture.
Long story short, if you change the position of the valves, you affect the indoor climate.
//
Let’s focus on this diagram. The chiller provides cold water to the AHUs, the AHUs provide cold air to the rooms. The rooms follow their dynamics, exchanging thermal energy among themselves and with the rest of the building.
As for the computers in ths system, we have four of them.
One local controller sitting on top of each AHU, and one general purpose computer stored in the Waiting room, inside a small rack, it runs all the complicated code, hosts a database and communicates with the external world whenever needed.

## Slide 26: System overview
Thermistor probes (x6)
Water flow sensors (x3)
Anemometers (x3)
Weather station
Z-wave sensors + Temp. probes (x10)
Servo motors (x3)
myRIOs (x3)
Mac Mini
Interface PCB (x3)
LAN
Z-WAVE
PHYS.
PHYS.
Actuators
Outputs
Disturbances
Disturbances
Notes: The local controllers are nothing but myRIO boards, programmed in LabView. For those of you that don’t know, LabView is a graphical language to program embedded platforms like this one.
The myRIOs were responsible for collecting data from a number of sensors: water flow sensors, water temperature probes, anemometers (measuring the air speed), and they were also responsible for driving the servo motors, hence turning the water valves.
Side note, since each of them operated in a sligtly different way, at different voltage levels, etc, I had to design this little PCB to interface the myRIOs and the sensors/actuators. And everything was connected using actual wires, carying out analog signals here and there.
/ /
Aside from that, we also had a weather station sitting on top of the building to measure the outdoor temperature and the solar radiation accurately.
To monitor the indoor temperatures, we deployed some 10 more sensors. We picked Z-wave temperature sensors and attached external temperature probes to them. These are really flexible since they are wireless and can operate autonomously for a couple of months before running out of battery.
Finally a Mac Mini, our main computer, that stored all the data and executed our control algorithms.
/ /
From a control engineering perspective, we could classify the elements you see on your screen as follows:
- The things that measure the system outputs
The things that measure your disturbances (exogenous signals that affect the system dynamics, but are not controlled by you)
And your actuators, the mechanism you have to influence the system
AND That’s all I had to say regarding the HW…

## Slide 27: Data collection and model training
Gaussian process NARX models:
Final delays:
Signals sampled at every 2 mins, but were downsampled by 5x to train the models (10 min)
Mixed training data: closed-loop PI, closed-loop RBC, open-loop random, open-loop ramps, etc
Final training set = 4’491 points (22’455 in total)
Pre-processing: outlier detection, imputing missing entries, discarding abnormal periods
Final number of samples per GP: 235, 314 and 245
“The most informative subset out of 748 hours”
ARD SE kernels + linear mean + MLE optimization
Notes: What did we do with all these data collected from the AHUs and rooms? We built models!
We have already explored GPs, correct? How do we use them to craft models for dynamical systems though?
A discrete-time dynamical system is simply a function predicting the future value of a certain variable as a function of past realizations of it – what is known as the autoregressive property.
If you allow this future value to depend on additional signals, say the position of a valve or the solar radiance, then we say the structure also accounts for exogenous signals.
Lastly, if this relationship F isn’t linear, we say the whole thing is an Nonlinear Autoregressive model with Exogenous Inputs.
/ /
Now if you don’t know F, you learn it from data using a GP… voila, you’ve got a GP-NARX model.
Everything inside the parenthesis is the features of our model, and the target variable is the temperature at the next time-instant.
The actual delays for each signal composing our final feature vectors can be found in the table down below.
That’s what you typically learn in a system identification class.
An extension of such framework is to allow the next variable to depend, not only on the immediately previous one, but on a couple of previous time-instants. That’s what we call an AR model.
Extension number 2, it can also depend on additional variables other than itself. Things we call ‘exogenous inputs’.
Put all that together and you have a NARX model!
If you use a Gaussian process to learn this function f from data, voila, you build your “GP-NARX” dynamical system model.
/ /
Everything that’s inside the parenthesis are the features of that GP, and the next temperature is the target variable. So now you also know how we had to organize your training dataset, right?
In order to choose the right delays
//
T_{i,t+1} = f(&T_{i,t}, T_{i,t-1}, \dots, T_{j,t}, T_{j,t-1}, \dots, \theta_{i,t}, \theta_{i,t-1}, \dots \\
&T_{\text{sup},t}, T_{\text{sup},t-1}, \dots, T_{\text{out},t}, T_{\text{out},t-1}, \dots, R_{\text{sol},t}, R_{\text{sol},t-1}, \dots )

## Slide 28: Training results
Notes: T_{i,t+1} = f(&T_{i,t}, T_{i,t-1}, \dots, T_{j,t}, T_{j,t-1}, \dots, \theta_{i,t}, \theta_{i,t-1}, \dots \\
&T_{\text{sup},t}, T_{\text{sup},t-1}, \dots, T_{\text{out},t}, T_{\text{out},t-1}, \dots, R_{\text{sol},t}, R_{\text{sol},t-1}, \dots )

## Slide 29: Test results
Notes: T_{i,t+1} = f(&T_{i,t}, T_{i,t-1}, \dots, T_{j,t}, T_{j,t-1}, \dots, \theta_{i,t}, \theta_{i,t-1}, \dots \\
&T_{\text{sup},t}, T_{\text{sup},t-1}, \dots, T_{\text{out},t}, T_{\text{out},t-1}, \dots, R_{\text{sol},t}, R_{\text{sol},t-1}, \dots )

## Slide 30: Test results
Notes: T_{i,t+1} = f(&T_{i,t}, T_{i,t-1}, \dots, T_{j,t}, T_{j,t-1}, \dots, \theta_{i,t}, \theta_{i,t-1}, \dots \\
&T_{\text{sup},t}, T_{\text{sup},t-1}, \dots, T_{\text{out},t}, T_{\text{out},t-1}, \dots, R_{\text{sol},t}, R_{\text{sol},t-1}, \dots )

## Slide 31: Learning the chiller energy curve
Final objective
Notes: 11 pts
\text{Q}(T_\text{out},\Theta) = &-3.15 \, T_\text{out} - 3.03 \,e^{-2} \, \Theta + 1.73\,e^{-1} \, T_\text{out}^2 - 1.56\,e^{-3} T_\text{out} \Theta \\
&+ 3.09\,e^{-4} \Theta^2 - 2.75\,e^{-3} T_\text{out}^3 + 4.90 \,e^{-4} T_\text{out}^2 \Theta \\
&- 6.86 \,e^{-5} T_\text{out} \Theta^2 + 2.56 \,e^{-6}\Theta^3 + 20.22
\text{COP}(Q) = 3.30 \, e^{-7} Q^4 - 2.69 \, e^{-5} Q^3 - 2.67 \, e^{-3} Q^2 + 2.34 \, e^{-1} Q^1 - 4.45 \, e^{-4}
E(T_\text{out},\Theta) = Q(T_\text{out},\Theta)/\text{COP}(Q(T_\text{out},\Theta))

## Slide 32: The NMPC formulation
Objective: minimize the electrical energy consumption
Prediction horizon of 12 steps = 2 hours
Total number of decision variables: 9N-4 = 104
No variance propagation
Slack variables to avoid infeasibility
Notes: \min & \quad \sum_{t=0}^{N-1} \left(E_t + \rho \Delta_t \right) + \rho_N \Delta_N\\
\text{s.t.}
& \quad T_{t+1} = \mu(T_t,\theta_t,T_{\text{sup}},T_{\text{out}}) \\
& \quad T_t + \beta \, \text{var}^{1/2} (T_t,\theta_t,T_{\text{sup}},T_{\text{out}}) \leq T_\text{max} + \delta_t \\
& \quad E_t = Q(T_\text{out},\Theta_t) / \, \text{COP}(Q(T_\text{out},\Theta_t)) \\
& \quad \theta_{\text{min}} \leq \theta_t \leq \theta_{\text{max}} \\
& \quad \delta_t \geq 0
\Theta_t = \sum_{i=1}^3 \theta_{t,i}
\Delta_t = \sum_{i=1}^3 \delta_{t,i}^2
\mu = \begin{bmatrix} \mu_1 \\ \mu_2 \\ \mu_3 \end{bmatrix}
\text{var} = \begin{bmatrix} \text{var}_1 \\ \text{var}_2 \\ \text{var}_3 \end{bmatrix}
\delta_t = \begin{bmatrix} \delta_{t,1} \\ \delta_{t,2} \\ \delta_{t,3} \end{bmatrix}
\theta_t = \begin{bmatrix} \theta_{t,1} \\ \theta_{t,2} \\ \theta_{t,3} \end{bmatrix}
T_t = \begin{bmatrix} T_{t,1} \\ T_{t,2} \\ T_{t,3} \end{bmatrix}

## Slide 33: The NMPC formulation
casADi + IPOPT on a 2.4 GHz, core i9 machine
Total number of GP data points
Warm starting the solver primal variables by using the nominal models and 3 PI controllers.

## Slide 34: Experimental results
Notes: We’re looking at a 4-day uninterrupted experiment conducted from Nov 10 to Nov 13.
Let me stress that out of the 5184 points, 43 missing entries (temps) that we had to impute. Everything else is precisely as reported by the sensors and the curves you see were NOT pre-processed in any way…

## Slide 35: Experimental results

## Slide 36: Experimental results

## Slide 37: Experimental results
“Fault”
“Fault”
Notes: You might be thinking, what is this weird behavior? The indoor temperatures are not high, and the valves are saturated at their low values!
If you look up a calendar, you’ll understand why. November 13 was a Saturday, and currently there are no surgeries scheduled for Saturdays. So that section of the building is almost unnocupied…
This truly gives us an idea of how strong the internal heat gains caused by people are in this application.

## Slide 38
Comparison among different techniques
The color scheme indicates the initial indoor temperatures: 17, 19 and 21 degrees Celsius.
The proposed MPC scheme reduced the energy consumption (monetary cost) by up to 3%, being always close to the optimal REF strategy.
Notes: Energy savings are next.

## Slide 39: Conclusion
Final remarks and future investigations
A complex case-study was presented, featuring multiple zones, strong disturbances, and an industrial forced-air cooling system within a hospital
The approach (GPs combined with MPC) guaranteed the indoor temperature regulation whenever enough actuation power was available with minimized energy consumption
Sparse Gaussian processes could be employed in the future to alleviate the computational load and enable the use of longer prediction horizons
To disseminate the technique and make it more attractive, a reliable and easy-to-use toolbox for designing and testing GP-NARX models is needed!
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 40: Part 3
Learning MPC controllers with pQP
neural networks
Published works:
Maddalena, Specq, Wisniewski, Jones. “Embedded PWM predictive control of DC-DC power converters via piecewise-affine neural networks.” IEEE OJIES (2021).
Maddalena, Moraes, Waltirch, Jones. “A neural network architecture to learn explicit MPC controllers from data.” IFAC World Congress (2020).
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 41: Introduction
The idea: Using tailored pQP activation functions as a bias in MPC learning via neural networks.
Motivation: Find simplified yet faithful representations of MPC mappings -> complexity reduction.
Can the user control the approximation complexity?
What level of accuracy can be achieved?
How does it compare to other complex. red. techniques?
Notes: Goal: introduce kernels and RKHSs

## Slide 42: Introduction
Goes from to
The network size is defined by the user.
Always feasible (w.r.t. ) and bounded from below
Ensures control feasibility
Parameters to be adjusted are shown in red.
Goes from to
Notes: Goal: introduce kernels and RKHSs

## Slide 43: Introduction
Intuition behind the proof: L1 and L2 (linear + pQP) learn the (condensed) MPC dual problem, and L3 implements the KKT stationarity condition that maps the optimal dual solution to the optimal primal solution.
L4 is not needed to arrive at the result, indeed, it acts as an identity map. However, it is crucial for deployment.
Once trained, L2 and L4 can be converted into PWA functions -> no need for the online solution of opt. problems.
Closed-loop stability guarantees can be verified a posteriori with mixed-integer programming.
Notes: Goal: introduce kernels and RKHSs

## Slide 44: System overview
GD
voltage
duty cycle
current
Clock: 80 MHz RAM: 128 kB Flash: 1 MB
GOAL: Attain a fast and non-oscillatory start-up response.

## Slide 45: System overview
Input DC source
Diode
Resistive load
Output capacitors
Inductor
Switch
Input signal goes here
Feedback signals

## Slide 46: Obtaining a model
Average dynamics over a switching period:
Linearization around a desired equilibrium point:
+ ZOH discretization (10 kHz)
Notes: x = \begin{bmatrix} x_1 \\ x_2 \end{bmatrix} = \begin{bmatrix} i_L \\ v_O \end{bmatrix}
u = \delta
&\dot x_1 = -\frac{R_L}{L} x_1 - \frac{1}{L} x_2 + \frac{V_{IN}+V_D}{L} u - \frac{R_{ON}}{L} x_1u - \frac{V_D}{L} \\
&\dot x_2 = -\frac{R_C R_O R_L C + R_O L}{(R_C+R_O)LC} x_1 - \frac{R_C R_O C + L}{(R_C+R_O)LC} x_2 + \frac{R_C R_O (V_{IN}+V_D)}{(R_C+R_O)L} u - \frac{R_C R_O R_{ON}}{(R_C + R_O)L} x_1u - \frac{R_C R_O V_D}{(R_C + R_O)L} \\
x_{1eq} = \frac{x_{2eq}}{R_O}
u_{eq} = \frac{R_O V_D + (R_L + R_O) x_{2eq}}{R_O(V_{IN}+V_D) - R_{ON}x_{2eq}}
\dot x = A_{ct}x + B_{ct}u
A_{ct} = \begin{bmatrix} -\frac{R_L + R_{ON} u_{eq}}{L} & -\frac{1}{L} \\[4pt] -\frac{R_C R_O (R_LC - R_{ON}Cu_{eq}+R_{O}L)}{(R_C+R_O)LC} & -\frac{R_C R_O C + L}{(R_C+R_O) LC}\end{bmatrix}
B_{ct} = \begin{bmatrix} \frac{V_{IN}+V_D-R_{ON}x_{1eq}}{L} \\[4pt] \frac{R_C R_O (V_{IN}+V_D-R_{ON}x_{1eq})}{(R_C+R_O)L} \end{bmatrix}

## Slide 47: Learning the MPC map
Standard linear MPC controller designed in MPT3. 5k samples (uniform distribution), nz = 3, weights initialized randomly, 5 re-initializations (35 min of computations each), final MSE loss of 1.66 x 10-7.

## Slide 48
Standard linear MPC controller designed in MPT3. 5k samples (uniform distribution), nz = 3, weights initialized randomly, 5 re-initializations (35 min of computations each), final MSE loss of 1.66 x 10-7.
Learning the MPC map

## Slide 49
Number of regions 70 -> 6, memory footprint 9.25 kB -> 528 B.
Learning the MPC map

## Slide 50: Results
Interrupt-driven code (100 us timer), 2 ADCs + DMA memory transfers, averaging over 8 samples (filtering), no floating-point variables.

## Slide 51: Results

## Slide 52: Results

## Slide 53: Results

## Slide 54: Conclusion
Final remarks and future investigations
A new neural network architecture was proposed to learn linear MPC controllers from data, featuring a pQP non-linearity, which was shown to be a suitable function class to accomplish the learning task
The non-linear layers can be transformed into PWA functions before deployment so that the NN evaluation does not require solving optimization problems
The final complexity can be controlled by the user by choosing a suitable network size
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 55: Conclusion
Final remarks and future investigations
A new neural network architecture was proposed to learn linear MPC controllers from data, featuring a pQP non-linearity, which was shown to be a suitable function class to accomplish the learning task
The non-linear layers can be transformed into PWA functions before deployment so that the NN evaluation does not require solving optimization problems
The final complexity can be controlled by the user by choosing a suitable network size
Theoretical future investigations could focus on linking the training loss directly to the worst-case approximation error, or even to closed-loop stability
From an experimental point of view, ML models could be used to learn more complex (e.g. MIQP) MPC formulations, which are popular in the fields that also require fast actuation (e.g. electrical drives)
Notes: Let Assumptions~\ref{as:kernel_spd_compact_X}-\ref{as.norm_bound} hold with $\bar \delta = 0$. Let $s$ be the minimum-norm interpolant $s(x)=\alpha^\top K_{Xx}, \alpha = y^\top K_{XX}^{-1}$. Then, for any $x \in \mathcal{X}$
\label{prop.noise_free_bound}
\begin{empheq}[box={\mymathbox[colback=black!2,drop small lifted shadow, sharp corners]}]{equation}
\label{eq.noise_free_bounds}
\left|s(x) - f^\star(x)\right| \leq P_X(x) \sqrt{\Gamma^2 - \rknorm{s}^2}
\end{empheq}

## Slide 56: Part 4
Final considerations
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 57
Chalet, Bujaroska, Germeni, Ghandri, Maddalena, Modi, Olopoenia, Thompson, Togninalli, Briggs.“Mapping the insomnia severity index instrument to EQ-5D health state utilities: A United Kingdom Perspective.” PharmacoEconomics-Open (2023).
Rosolia, Lian, Maddalena, Ferrari-Trecate, Jones. “On the optimality and convergence properties of the iterative learning model predictive controller.” IEEE Transactions on Automatic Control (2022).
Chakrabarty, Maddalena, Qiao, Laughman. “Scalable Bayesian optimization for model calibration: Case study on coupled building and HVAC dynamics.” Energy and Buildings (2021).
Maddalena, Jones. “NSM converges to a k-NN regressor under loose Lipschitz estimates.” IEEE Control Systems Letters (2020).
Maddalena, Jones. “Learning non-parametric models with guarantees: A smooth Lipschitz regression approach.” IFAC-PapersOnLine (2020).
Part 4
Published works that were not discussed in this thesis
Notes: Mathematically,
Let’s assume you have an underlying function that you want to model, F.
You perform some experiments, collecting some pairs of (x,y), where the ys carry information about F are corrupted by additive noise, which is distributed Normally with zero mean and some standard deviation SIGMA.
GPs are defined following Bayesian statistics principles. Firstly, you specify what is known as a PRIOR for unknown values of F. Something that encapsulates your personal beliefs about it – and yes, that’s subjective.
This PRIOR must be in the form of a Gaussian as well, where you can specify its mean and covariance.
Next, in combination with your data, you apply Baye’s rule (Baye’s theorem) to derive the POSTERIOR expression for F – which then defines your Gaussian process.
The beauty of GPs is that this step can be carried out analytically, and there’s almost no other setting in which this is true. Which means, there are no approximations being made when deriving GPs!
If all of this is unfamiliar to you, just remember the following two equations.
The first defined your nominal predictions, whereas the second will give you the level of uncertainty for that same prediction.
In other words, if we come back to this picture…
- - - -
y_i = f(x_i) + \varepsilon_i, \ i=1,\dots,N
\epsilon_i \sim \mathcal{N}(0,\sigma)
f(x) \sim \mathcal{N}(m(x),k(x))
p(f) = \mathcal{N}(m(x),k(x))
p(f\,|y) = \mathcal{N}(\mu(x),\text{var}(x))
\mu(x) &= m(x) + k_X(x)^\top (K_{XX}+\sigma^2I)^{-1}(y-m_X)
\text{var}(x) &= k(x,x) - k_X(x)^\top (K_{XX}+\sigma^2I)^{-1} k_X(x)

## Slide 58: Part 4
Concluding remarks
Final research output: 7 journal papers and 5 conference papers.
Throughout my doctoral studies, I have explored three different domains, contributing to them by:
Proposing a novel uncertainty quantification framework and illustrating how it could be used by the control community
Validating the use of GP-based MPC to tackle the temperature control of a building with a complex cooling system
Putting forward a new linear-MPC complexity reduction scheme based on a tailored NN architecture

## Slide 59
Thank you for your attention